Good vibrations: Modal Dynamics for Graphics and Animation

Goal: Use interactive dynamic simulation of multi-body situations to aid in physical design

Idea: Describe geometry and dynamics separately, then couple representations
- Dynamics: vibration-mode (“modal”) representation
- Geometry: volumetric model (superquadrics)
→ Combined using polynomial deformation mapping

MODAL ANALYSIS

Modal analysis: method of breaking non-rigid dynamics down into sum of independent vibration modes

Finite element method (FEM): technique for simulating the dynamic behavior of an object
1) Continuous variation of displacements replaced by finite number of displacement at nodal points
2) Interpolated using smooth function
→ Solve nodal unknowns using energy equations (functionals) (cf eq.1): can be interpreted as assigning a mass to each nodal point, a material stiffness btw nodal points, a damping as dashpots btw nodal points.

- Whitening transform (cf eq.2) used to get independent differential equations, which simultaneously diagonalizes M, D, K (cf eq.4)
- Explicit solutions of inverse dynamics (cf eq.8, 11)
- Each equation represents one mode (Mi inertia, Di damping, Ki spring stiffness, fi force)
- i-th row of ϕ describes deformation of object in response to fi
- λi proportional to the natural resonance frequency of the i-th vibration mode

Rq: Non-linear material may be modeled by summing modes at the end of each time step to form material stress state, which can then be used to drive non-linear plastic or viscous material behavior

OPTIMIZATION

Increased Speed + Larger time steps: modes associated with high resonance frequencies normally have little effect on object shape
→ Discard small-amplitude (= high frequency) modes by examining eigenvalue
(Find which modes to add determined by PCA on error residuals)
→ Restrain to rigid-body (0th order), linear (1st order), quadratic (2nd order) strain modes for simple objects
- Temporal aliasing: reduced by discarding high frequencies
- Approximate modes: sufficient to use precomputed deformation modes, parameterized only by object’s low order moments of inertia
→ Precompute deformation modes using a simple 3D parabolic element (20 nodal points) to approximate the shape

COMBINE DYNAMICS AND ANALYTIC GEOMETRY
Describe each mode by polynomial function (cf eq.5), then establish correspondence btw dynamic state and geometric state using global deformation techniques
→ Scale polynomial deformation according to mode’s amplitude

COLLISIONS
Inside-outside function of superquadrics (cf eq.7)

CONTROL OF ANIMATION
Control knobs for stretch/squash
- Amplitude = Speed (cf Fig 7)
- Amplitude = Speed – Acceleration (cf Fig 8)
- Amplitude link to position (cf Fig 9)

Results
- Gain of 2 orders of magnitude in efficiency
- Control temporal aliasing
- Simple, closed-form solutions to common non-rigid inverse dynamics problems
- Ease collisions